# JI-111C IP indoor/outdoor camera 2MP - DOME

Video verification cameras provide the user and PCO with a visual confirmation of the alarm reason and show what is going on in the building. Any event is automatically recorded so the user is in the picture when something happens.

## JI-111C IP indoor/outdoor camera 2MP - DOME

A big advantage is an easy installation of the cameras even without an advanced knowledge of IT technologies. They are fully integrated into the MyJABLOTRON application and cooperate with the JABLOTRON 100 system through Cloud. The customer has thus all the information about his or her premises clearly available in one place.

The camera takes colour videos in HD or Full HD resolutions. In case of poor light conditions it switches to a night mode using IF (Infrared) lighting.

## Basic function of the camera:

- Video sequences

  - Video recording of 30 sec. before the event  (eg. alarm or security) and 30 sec. after it.

  - It clearly shows what caused the event and what happened immediately afterwards.

  - The user can also request its creation from the MyJABLOTRON application.

- Record

  - Continuous video saving with an optional history (3 or 7 days).

  - A full history is at the user´s disposal; he or she can check it any time to find out what happened in the building at a particular moment.

- Live video

  - It can be started from the web or mobile versions of the MyJABLOTRON application.

  - At any time, the user can check what is going on in the building.

Under a normal internet connection, it takes ca. 10 sec. to connect to the camera.

## Technical specifications

| Power supply | 12 V DC alternatively from the data connection PoE 802.3 af (48V) power consumption in day (at rest): 200 mA power consumption at night (with IR lighting): 350 mA |
| --- | --- |
| Number of pixels | 2 Mpix |
| Camera resolution | 1920*1080 points |
| Camera lens | Dome 2,8 mm (viewing angel 115°) |
| Lens type | Mono |
| Sensor | 1/2,8" CMOS |
| Lens rotation options | 0°- 355° |
| Communication interface | RJ-45 10M/100M Ethernet |
| IR lighting angel | 70° |
| IR lighting reach | max. 30 meters (12x IR LED) |
| Surroundings | IV. outdoor general (according to the ČSN EN 50131-1 standard) |
| Range of operating temperatures Dome | From -20 to +55 °C, max. humidity 75% |
| Degree of protection | IP67 |
| Dimensions | 111 x 111 x 82 mm |
| Weight | 500 g |

# JI-112C IP indoor/outdoor camera 2MP - BULLET

Video verification cameras provide the user and PCO with a visual confirmation of the alarm reason and show what is going on in the building. Any event is automatically recorded so the user is in the picture when something happens.

## JI-112C IP indoor/outdoor camera 2MP - BULLET

A big advantage is an easy installation of the cameras even without an advanced knowledge of IT technologies. They are fully integrated into the MyJABLOTRON application and cooperate with the JABLOTRON 100 system through Cloud. The customer has thus all the information about his or her premises clearly available in one place.

The camera takes colour videos in HD or Full HD resolutions. In case of poor light conditions it switches to a night mode using IF (Infrared) lighting.

## Basic functions of the camera:

- Video sequences

  - Video recording of 30 sec. before the event (eg. alarm or security) and 30 sec after it.

  - It clearly shows what caused the event and what happened immediately afterwards.

  - The user can also request its creation from the MyJABLOTRON application.

- Record

  - Continuous video saving with an optional history (3 or 7 days).

  - A full history is at the user´s disposal; he or she can check it any time to find out what happened in the building at a particular moment.

- Live video

  - It can be started from the web or mobile versions of the MyJABLOTRON application.

  - At any time, the user can check what is going on in the building.

## Technical specifications

| Power supply | 12 V DC alternatively from the data connection PoE 802.3 af (48V) power consumption in day (at rest): 200 mA power consumption at night (with IR lighting): 350 mA |
| --- | --- |
| Number of pixels | 2 Mpix |
| Camera resolution | 1920*1080 points |
| Camera lens | Bullet 4 mm (viewing angel 90°) |
| Lens type | Mono |
| Sensor | 1/2,8" CMOS |
| Lens rotation options | 0°- 355° |
| Communication interface | RJ-45 10M/100M Ethernet |
| IR lighting angel | 70° |
| IR lighting reach | max. 50 meters (12x IR LED) |
| Surroundings | IV. outdoor general (according to the ČSN EN 50131-1 standard) |
| Range of operating temperatures Bullet | From -20 to +55 °C, max. humidity 75% |
| Degree of protection | IP67 |
| Dimensions | 300 x 90 x 90 mm |
| Weight | 500 g |